Common Wood Beams
Don Peterson Words: 4775
someonesdad1@gmail.com 21 May 2020
This document discusses the wood.py python script, which prints out properties of common sizes of Douglas fir material used in the US. If you don't want to use the python script, you can still use the material the script outputs for hand calculations (see the Hand calculations section).
The package you'll download is wood.zip which includes this document and the python accessory modules necessary for running the script. The sig.py and u.py modules are required; the color.py module is optional and will show stresses that exceed the modulus of rupture in color on your terminal. The script requires python 3.6 or later to run and must be run from a console. Unzip the wood.zip file in a directory and run the script with python wood.zip to get a help message.
Why you might want to use this script: I use this script to estimate beam bending stress when using a board or to select a beam size given a length and load. It also gives me the mass of a beam and section properties. By default it covers US boards in 2x2, 2x4, 2x6, 2x8, 2x10, and 2x12 sizes as these are commonly-used sizes in the US, the -m option adds some "4 by" beams. It's easy to change the script to report on any board sizes you wish (change the sizes dictionary at the beginning of the script).
# Notation
I've used inches and pounds in the script because they are common when working with this stuff and contractors/store clerks go catatonic if you give them a dimension in millimeters or newtons.
The term pound is abbreviated lb and is technically a mass of about 0.45 kg. In speech, most of us say pound and mean it to be either a mass of one pound or the weight of a one pound mass at the Earth's surface. The force unit of one pound is usually designated lbf in more careful work to indicate it's a force -- and it's also helpful to designate the mass unit as lbm.
psi measures pressure and stress and is an abbreviation for pounds force per square inch, a force per unit area. kpsi uses the SI k for kilo abbreviation, which means 1000. Thus, kpsi means one thousand pounds per square inch.
A reference is given as [xxx] where xxx is an abbreviation. [xxx:p] means page number p in the reference and [xxx:p:q] means the document is a PDF and page p in the text corresponds to page q in your PDF client viewer.
## Informational use only
The wood.py script and this documentation are for informational use only. You should consult a professional engineer for a proper design if the failure of a wood structure could result in injury, death, property damage, or economic loss.
# Script usage
If the script is run with no parameters, the following message is printed:
Usage: wood.py [options] [length load]
  Print deflection and stress properties for beams from common Douglas
  fir wood commonly used in the US of the given length and uniform load.
  You can include common unit abbreviations with the numbers with no
  separating space (example: 12ft). If no arguments are given, a table
  of properties is printed (use -f to include formulas).

  The results are printed to 2 significant figures. Formulas are from
  the 19th edition of Machinery's Handbook.

Options:
  -c Beam load is concentrated at one point
  -d n Number of significant figures
  -e Show some design examples
  -f Include beam formulas when printing table
  -l Neutral axis is parallel to long axis
  -m Include more board sizes
  -s n Specify the rupture stress (n can be an expression)
  -t Print table of beam properties
The main tasks done with the script are 1) to print out beam properties for a given length and load and 2) print a table of "2 by" wood properties.
## Table of properties
Use the command python wood.py -t to get a table of data:
Table of Douglas fir lumber (specific gravity = 0.5)
Neutral axis parallel to short edge

      Width, Height, Mass, A, I, Y, Z, k,
Size in in lbm/in in2 in4 in in3 in
---- ------ ------ ------ ------ ------- ----- ------- -----
2x2 1.5 1.5 0.041 2.2 0.42 0.75 0.56 0.43
2x4 1.5 3.75 0.10 5.6 6.6 1.9 3.5 1.1
2x6 1.5 5.5 0.15 8.2 21 2.8 7.6 1.6
2x8 1.5 7.25 0.20 11 48 3.6 13 2.1
2x10 1.5 9.25 0.25 14 99 4.6 21 2.7
2x12 1.5 11.25 0.30 17 180 5.6 32 3.2

  A = cross-sectional area
  I = moment of inertia
  Y = location of neutral axis from short edge
  Z = section modulus
  k = radius of gyration
This table is useful when doing hand calculations (see the Hand calculations section). It is for a beam whose neutral axis is parallel to the short edge (e.g., a joist).
If you want the table for when the neutral axis is parallel to the long edge (e.g., a plank), add the -l option to get the table
Table of Douglas fir lumber (specific gravity = 0.5)
Neutral axis parallel to long edge

      Width, Height, Mass, A, I, Y, Z, k,
Size in in lbm/in in2 in4 in in3 in
---- ------ ------ ------ ------ ------- ----- ------- -----
2x2 1.5 1.5 0.041 2.2 0.42 0.75 0.56 0.43
2x4 3.75 1.5 0.10 5.6 1.1 0.75 1.4 0.43
2x6 5.5 1.5 0.15 8.2 1.5 0.75 2.1 0.43
2x8 7.25 1.5 0.20 11 2.0 0.75 2.7 0.43
2x10 9.25 1.5 0.25 14 2.6 0.75 3.5 0.43
2x12 11.25 1.5 0.30 17 3.2 0.75 4.2 0.43

  A = cross-sectional area
  I = moment of inertia
  Y = location of neutral axis from long edge
  Z = section modulus
  k = radius of gyration
## Beam properties
Suppose you need a beam to support a uniformly distributed load along its short edge (like a floor joist). The load is 1000 lbf and the beam length is 8 feet. What size beam should you use if the beam is supported at the ends?
Use the command python wood.py 8ft 1000 to get the report
Loaded beam results
  Douglas fir with specific gravity of 0.5
  Length = 96 inches = 8.0 feet
  Load = 1000 lbf (uniform)
  y = maximum deflection in inches
  s = maximum stress in psi
Beam configurations (beam has a uniform load and is horizontal):
  Fixed Fixed at both ends
  Supported Supported at both ends
  Cantilevered Fixed at one end
Rupture stress = 12000 psi, weight of board is ignored

      Mass Fixed Supported Cantilevered
       lb y, in s, psi y, in s, psi y, in s, psi
      ----- --------- --------- --------- --------- --------- ---------
2x2 3.9 4.6 7100 23 21000 220 85000
2x4 9.8 0.29 1100 1.5 3400 14 14000
2x6 14 0.092 530 0.46 1600 4.4 6300
2x8 19 0.040 300 0.20 910 1.9 3700
2x10 24 0.019 190 0.097 560 0.93 2200
2x12 29 0.011 130 0.054 380 0.52 1500

Column characteristics

      Compression Critical force
        psi buckling, klbf
      ----------- ---------------
2x2 440 2.2
2x4 180 34
2x6 120 110
2x8 92 240
2x10 72 510
2x12 59 910
Looking under the Supported column, we see that a 2x4 would have a bending stress of 3400 psi from this load and a deflection at the center of 1.5 inches. Since the rupture (breaking) stress is approximately 12 kpsi, the 2x4 would work for a static load. A larger width would have less deflection.
The Column characteristics section gives the compression or tension stress in a beam with the indicated load applied longitudinally (typically the grain is in the longitudinal direction). The critical force is for a column fixed on both ends and is the load where the column will start to buckle (see [wpecl]).
The script only prints out answers to 2 significant figures. More digits don't make sense because these are estimates only and will be influenced by many things like the condition of the wood, knots, moisture content, loads that aren't static, etc. If you want more digits in the answers, use the -d n option where n is the number of digits. Note you may overflow the report column sizes, but this can still be handy for checking calculation details.
# Wood properties
Most folks know from experience that wood has different properties in different directions. For example, a screw driven across the grain holds well, while a screw driven parallel to the grain (e.g., in end grain) doesn't hold nearly as well. Contrast this to a material like steel, which has the same properties in any direction.
A graph used to understand the mechanical properties of a material is the stress-strain curve. This curve tells you how much a material changes its length under an applied force. The terms stress and strain are normalized values. Stress is normalized by dividing the force by the area of the piece the force is applied to (so a stress is a pressure). Strain is the amount of movement divided by the length of the piece and is thus dimensionless.
Figure 1shows a stress-strain curve for a low carbon steel [wpss].
Most use of the steel is in the area where the stress and strain are less than the yield point. The curve in this area is straight and is often called the proportional region because the increase in length (strain) is proportional to the stress (i.e., the rise/run or slope is constant). The proportional region is due to the stretching of the electrostatic bonds between the material's atoms which relax back to their original position when the force is removed.
Figure 1
At the yield point, the length can increase with no applied force. This is where the material inelastically deforms and, if the force is removed, the piece retains a set, meaning it is longer than before the force was applied. You've undoubtedly seen this behavior with a helical spring. The atoms of the material have had some of their electrostatic bonds stretched so much that some of the atoms have moved, permanently changing the shape of the material.
The ultimate strength is the highest strength of the material and past this point the sample increases in length with a reduction in cross-sectional area (necking) until the part fractures.
A stress-strain curve for wood in bending behaves qualitatively similarly, but doesn't typically have the yield point, set, or necking -- the wood just fractures. Here's a sketch based on figure 4.26 in [ho]; the axes are linear from zero:
The nonlinear behavior above the proportional limit is caused by atoms of the material being moved from their original positions. This type of test is typically done as shown in Figure 3.
Figure 2
You've probably experienced this type of behavior when you step on a twig and break it. You'll know from experience that you can press harder and harder on the twig and it will return to its original shape when you remove the force. But if you go a bit too far, you'll hear a crack and know that you've reached the fracture point. If the twig didn't fracture all the way through, it can still have proportional behavior, but the deflection will be larger for a given force than before the twig was broken.
Figure 3
This document discusses beams with a rectangular cross section as shown in Figure 4.
If up is as indicated, this might be a 2x4 on its edge as if it was being used as a joist. If the beam was turned 90° about an axis normal to the page, then it would be a plank. I'll designate the first orientation as "neutral axis parallel to short side" and the second orientation "neutral axis parallel to long side".
The neutral axis is where the stresses are zero in bending. When the force is applied to the top of the beam, figure 4.24 in [ho:88] shows how the portion of the beam above the neutral axis is in compression and the portion below the neutral axis is in tension (stretched). This results in a shearing action along the neutral axis. The picture in figure 4.27B in [ho:89] nicely shows the compression and tension failures in a beam that failed in bending.
Figure 4
The basic equations for these beams are
y `prop` {F L^3} over {E I} `prop` {F L^3} over {E b d^3}	(1)

and
s `prop` {F L} over Z `prop` {F L} over {b d^2}	(2)

where ∝ means "proportional to" and
F = load (force) applied to beam, lbf
E = modulus of elasticity of beam material, psi
s = stress, psi
y = deflection at center of beam, inches
I = moment of inertia
Z = section modulus
d = beam height
b = beam width
L = beam width
The terms in the equations with exponents higher than one are where you should focus your efforts first if you need to reduce deflection or stress because they give the most bang for the buck.
- To reduce deflection, reduce the beam length L or increase the beam height d.
- To reduce stress, increase the beam height d.
Of course, you may not be able to change these things because of problem constraints, so you then see how you can change the other variables in the equations.
## Modulus of elasticity
The modulus of elasticity quantifies how stiff a material is: the higher the modulus, the more stress (force per unit area) it takes to make the material deflect. For wood, the modulus in the longitudinal direction is the number that's usually of interest (see Figure 5, taken from [wh]).
To give you a feel for this number, here are some approximate values in Mpsi:
Figure 5
Rubber	0.01
Teflon	0.08
Nylon	0.04
Medium density fiberboard	0.6
Wood, along grain (longitudinal)	1.6
Bone	2
Concrete	4
Glass	10
Aluminum	10
Brass	16
Steel	30
Tungsten carbide	80
Diamond	160

[wh] gives the following properties for the different Douglas fir species in the green and 12% moisture states, rounded to two figures:
	Specific gravity		E, Mpsi		MOR, kpsi
Species name	Green	12%	Green	12%	Green	12%
Coast	0.45	0.48	1.6	2.0	7.7	12
Interior west	0.46	0.50	1.5	1.8	7.7	13
Interior north	0.45	0.48	1.4	1.8	7.4	13
Interior south	0.43	0.46	1.2	1.5	6.8	12

E is the modulus of elasticity and MOR is the modulus of rupture. MOR is an estimate of bending stress where the wood breaks.
For the script's predictions, I've assumed 12% moisture and chosen the following values:
E = 1.7 Mpsi
MOR = 12 kpsi
Specific gravity = 0.48
You'll want to adjust things appropriately if you know the wood has more moisture than the 12% value assumed. In recent years, the demand for wood has made vendors use woods that are not very well dried. I've purchased wood posts for fencing that were so wet that water dribbled out of the screw holes when I put in a screw. For careful predictions, take a sample of the wood from the stuff you're using, support it, put a load in the middle, and measure the deflection, then compare it to the script's output.
## Change geometry
Suppose you had plenty of 2x6 material on-hand, but a single board wasn't strong enough for the load. A straightforward fix could be to glue and screw two of these boards together with their long sides touching. If the attachment is rigid, this will halve the deflection and stress, although now the beam weighs and costs twice as much.
A better fix would be to attach them with the short sides in contact as this doubles d, which is where you should first focus your efforts because of its non-unity exponent. However, this is more difficult unless you use things like steel joining plates or long screws (say, about 8 inches long) to pull the two boards tightly together (you can get Torx drive bugle head screws in such lengths). Make sure to use a good glue before screwing the boards together. This should reduce the deflection by a factor of 8 and the stress by a factor of 4. If you glued and screwed a 2x4 to the 2x6, the beam height d would increase from 5.5 to 9, so the deflection would reduce by (9/5.5)3 or 4.4 and the stress would reduce by 2.7.
Example: To join a 2x4 to a 2x6, I'd use some 6 inch long #1 Torx bugle head screws and a suitable glue. In May 2020 we bought some of these screws at 25 cents each. After gluing the two board edges, I'd clamp them together with a screw every 6 inches, so the increased beam cost would be my labor, 50 cents per foot for the screws, and the adhesive. Typical glues (except epoxies) can take 24 hours to cure, so there's also a project delay of a day. If I didn't have a waterproof glue, I'd also want the beam to be painted to keep water out of the glue if the beam was to be used outside.
Another tactic is to change the beam shape to e.g. an I-beam as shown in Figure 6.
The moment of inertia is
Figure 6
I `=` {bd^3 - h^3(b-t)} over 12	(3)

Using three 2x6s for this I beam would give a moment of inertia of
I `=` {5.5(8.5^3) - 5.5^3(5.5-1.5)} over 12 `=` 226 " in"^4	(4)

If two 2x4s were used for the end pieces, the moment of inertia would be 151 in4, seven times the plain 2x6 value.
This is an order of magnitude increase in the moment of inertia of a single 2x6 beam. Of course, the weight and cost have tripled and the height has increased 3 inches.
Commercial I-joists are available that could be made in a home shop (see here for a picture).
# Hand calculations
The table data and the formulas can be printed with the command python wood.py -fl:
Table of "2 by" Douglas fir lumber
Thickness is 1.5 inches, specific gravity is 0.5
Neutral axis parallel to short edge

       Width, Mass, A, I, Y, Z, k,
Size in lbm/in in2 in4 in in3 in
---- ------ ------ ----- ------ ----- ----- -----
2x2 1.5 0.041 2.25 0.42 0.75 0.56 0.43
2x4 3.75 0.102 5.62 6.59 1.88 3.52 1.08
2x6 5.5 0.149 8.25 20.80 2.75 7.56 1.59
2x8 7.25 0.196 10.88 47.63 3.62 13.14 2.09
2x10 9.25 0.251 13.88 98.93 4.62 21.39 2.67
2x12 11.25 0.305 16.88 177.98 5.62 31.64 3.25

  A = cross-sectional area
  I = moment of inertia
  Y = location of neutral axis from short edge
  Z = section modulus
  k = radius of gyration

Beam formulas
   F = load in lbf
   d = beam height, inches
   b = beam width, inches
   L = beam length, inches
   y = maximum deflection of beam, inches
   s = maximum stress in psi (psi = lbf/inches**2)
   E = Young's modulus = 1.2e+06 psi for Douglas fir
   I = moment of inertia = b*d**3/12 inches**4
   Z = section modulus = I/Y = b*d**2/6 inches**3
   Y = distance to neutral axis = d/2 inches
   α = F*L**3/(E*I)
   β = F*L/Z

        b
        +-------+
        | |
        | |
        | |
        d |-------| -----
        | | ^
        | | Y
        | | v
        +-------+ -----

Uniform load
  Fixed at both ends
     y = α/384
      s = β/24
  Supported at both ends
      y = 5*α/384
      s = β/8
  Cantilevered (fixed at one end)
      y = α/8
      s = β/2
Load concentrated at one point
  Fixed at both ends, load at center
      y = α/192
      s = β/8
  Supported at both ends, load at center
      y = 5*α/384
      s = β/2
  Cantilevered (fixed at one end), load at unsupported end
      y = α/3
      s = β
The beam equations cover two loading situations: a distributed load (uniformly across the surface of the beam) and a concentrated load at a point.
Here are the three beam conditions covered:
The fixed end is where the end of the beam is tightly attached to a rigid structure by e.g. screws, bolts, or glue. For example, the legs of a sawhorse are screwed to a beam, meaning the beam's ends are fixed. A scaffold board end sitting on two sawhorses is an example of supported beam ends.
Figure 7
# Unphysical inputs
You have to use good judgment and common sense when using the script or formulas. For example, suppose we calculate the beam properties of a 1 mile long beam with a 1 lbf load. The command is python wood.py 1mile 1 and the results are:
Loaded beam results
  Douglas fir with specific gravity of 0.5
  Length = 63000 inches = 5300 feet
  Load = 1.0 lbf (uniform)
  y = maximum deflection in inches
  s = maximum stress in psi
Beam configurations (beam has a uniform load and is horizontal):
  Fixed Fixed at both ends
  Supported Supported at both ends
  Cantilevered Fixed at one end
Maximum allowed stress = 12000 psi, weight of board is ignored

      Mass Fixed Supported Cantilevered
       lb y, in s, psi y, in s, psi y, in s, psi
      ----- --------- --------- --------- --------- --------- ---------
2x2 2600 1.3e6 4700 6.5e6 14000 6.3e7 56000
2x4 6400 84000 750 420000 2300 4.0e6 9000
2x6 9400 27000 350 130000 1000 1.3e6 4200
2x8 12000 12000 200 58000 600 560000 2400
2x10 16000 5600 120 28000 370 270000 1500
2x12 19000 3100 83 16000 250 150000 1000

Column characteristics

      Compression Critical force
        psi buckling, klbf
      ----------- ---------------
2x2 0.44 5.0e-6
2x4 0.18 7.8e-5
2x6 0.12 2.5e-4
2x8 0.092 5.6e-4
2x10 0.072 0.0012
2x12 0.059 0.0021
Look at the results for the 2x2 under the Supported column: the deflection y in the middle of the beam is longer than the beam. For the 2x4, the stresses are below the rupture point, but the model is grossly wrong since the mass of the beam is 6400 lbm. If you change the arguments to 1mile 6400, the deflections y and stress values s are insanely unphysical.
A "simple" problem like a 100 lbf load on an 8 foot long 2x4 is pretty easy to imagine and you'd probably trust the results of the script. But increase either of the arguments (length or force) and you are moving more towards the insanely unphysical region. Where do things get unphysical? You'll have to learn by experiment to get to the truth and use your or others' judgments for the in-between areas.
A real world problem will involve 1) the load on the beam, which the script assumes has no mass, and 2) the weight of the beam. You can model the weight of the beam as a uniformly applied force, but you'll have to figure out how to combine the results from the external load and the weight load. I don't deal with such things, as I use the script to analyze forces that are substantially larger than the weight of the beam and thus ignore the beam weight.
# Sample problems
This section has sample problems that illustrate the use of the script.
## Standing on a 2x4
This is intended to give a feel for the reasonableness of the program's predictions. If I support an 8 foot long 2x4 on two ladders (e.g., a scaffold) and I weigh 180 lbf, what will be the deflection and stress if I stand on the long edge in the middle of the board? The situation is illustrated in Figure 8.
Method of solution: Look for the data under the Supported column. The arguments are -c -l 8ft 180.
Figure 8
Results: (column characteristics omitted)
Loaded beam results
  Douglas fir with specific gravity of 0.5
  Length = 96 inches = 8.0 feet
  Load = 180 lbf (concentrated)
  y = maximum deflection in inches
  s = maximum stress in psi
Beam configurations (load is concentrated at one point):
  Fixed Fixed at both ends, load at center
  Supported Supported at both ends, load at center
  Cantilevered Fixed at one end, load at unsupported end
Maximum allowed stress = 12000 psi, weight of board is ignored

      Mass Fixed Supported Cantilevered
       lb y, in s, psi y, in s, psi y, in s, psi
      ----- --------- --------- --------- --------- --------- ---------
2x2 3.9 1.6 3800 4.1 15000 100 31000
2x4 9.8 0.66 1500 1.6 6100 42 12000
2x6 14 0.45 1000 1.1 4200 29 8400
2x8 19 0.34 790 0.85 3200 22 6400
2x10 24 0.27 620 0.66 2500 17 5000
2x12 29 0.22 510 0.55 2000 14 4100
Answer: The beam deflects 1.6 inches under where I stand and the stress is about half of the rupture value. You can increase the load to find that rupture will occur at about 350 pounds with 3.2 inches of deflection. I might be able to break the board by jumping up and down on it with one foot.
## Sawhorse
A 4 foot long 2x6 is used to make a sawhorse beam. What are the maximum loads for this beam if the ends are fixed?
Method of solution: find the load that results in the rupture stress allowed under the Fixed results. Invoke with the arguments 4ft X where X is the load value until the 2x6 entry for s under Fixed is greater than 12 kpsi. Compare the uniformly loaded value to the concentrated value by using the -c option.
Answers: About 45 klbf for a uniform load and a third of this for the concentrated load.
## Scaffold beam
I need to stand on a scaffold beam that is 16 feet between supports. If my equipment and I weigh 250 lbf and I stand in the center of the beam, what wood width should I use to not exceed the maximum allowed wood bending stress of one fourth of the rupture stress (12000/4 or 3000 psi)? The situation is the same as illustrated in Figure 8 but with different values and the beam size needs to be determined.
Method of solution: The load is concentrated at the center, so use the -c option. You also need to use the -l option because you'll be standing on the long side of the beam (i.e., a plank). We need to specify the maximum stress to be 3000 psi, so the -s option is used. The script arguments are -c -l -s 3000 16ft 250.
Answer: With the indicated arguments, the stress s under the Supported column was above the desired 3000 psi for all "2 by" planks. The stress is proportional to the force and beam length, so our choices are to 1) decrease the length of the beam, 2) reduce the load, or 3) reduce the factor of safety (i.e., allow more bending stress). Since we know the stress from the above arguments is near 6000 psi, twice what we want, we can halve the length of the beam and be able to use a 2x12.
Some folks increase the force by 50% to account for the dynamic force of a person walking on the plank. You can increase the moment of inertia of the plank by tightly screwing e.g. a 2x8 on end to the center of the bottom of the 2x12.
## Cantilever
I want to support load F in the center of a beam A parallel to a wall and with two identical cantilever beams B and C fixed to the wall supporting the ends of beam A. Beam A's ends are screwed to the ends of beams B and C. What beam sizes should I use? Suppose
F = 500 lbf
Beam A length = 10 ft
Beam B and C lengths = 6 ft
Figure 9 shows the details.
Method of solution: There are two separate problems:
Figure 9
First, you need to determine the size of beam A. This is done as in the scaffold problem above with the arguments -l -c 10ft 500. Under the Fixed column, we'd pick the 2x4.
Second, the load on each cantilevered beam will be half of 500 lbf plus the weight of the 2x4 or 262 lbf. Use the arguments -c 6ft 262 and the Cantilevered stress value will be acceptable if you use a 2x4. The load must be on the short side of the beam.
Comment: if this were a permanent structure, you might want to use the 10-year design stress levels given in [wh]. These are on the order of one-tenth the rupture stress. Aiming for around 1200 psi stress, you'd choose a 2x12 for beam A and a 2x8 for beams B and C.
# References
wh	Wood Handbook, US Forest Service, FPL-GTR-190, April 2010.
mh	Machinery's Handbook, Industrial Press, 19th ed. 1971.
ho	R. Bruce Hoadley, Understanding Wood, 2nd ed., Taunton Press, 2000.
wpss	Wikipedia's article on stress-strain curves, https://en.wikipedia.org/wiki/Stress%E2%80%93strain_curve, accessed 21 May 2020.
wpecl	Wikipedia's article on Euler's column formula, https://en.wikipedia.org/wiki/Euler%27s_critical_load, accessed 22 May 2020.
aw	https://amesweb.info/Materials/Youngs-Modulus-of-Wood.aspx, accessed 23 May 2020.