Holes on a circle
someonesdad1@gmail.com 20 Jan 2013
Updated 13 Oct 2019

This documents a python script called holes.py that calculates how you must place a set of circles on a main circle in order to have a constant angular gap between the circles; this can produce a visually-pleasing layout. An example would be to construct a holder for a set of drills or punches.
The input to the program is a file containing the diameters of the desired circles in the order you want them to appear around the main circle. You also give the diameter of the main circle on the command line (units are not needed; it is assumed all dimensions are in the same units, as are the output numbers). Here's an example invocation to place some circles defined in datafile on a circle of 148 units in diameter:
python holes.py datafile 148
While this script doesn't do anything you can't do manually with a calculator and piece of paper, it has the advantage of letting you tweak things to get the solution you want. For example, if you performed a manual calculation for 15 holes, then decided you wanted a slightly larger main circle and wanted to change two of the circle's diameters, you'd have to do the calculation all over again. The script can do it in a fraction of a second.
If you're willing to download an optional python graphics library, you can get a plot of the locations and dimensions to see what the finished layout looks like.
Update 13 Oct 2019: I added the -l option, which calculates the hole locations for holes in a line. An example is when making a block of wood to hold a set of sockets: you want the holes' edges to be separated by a constant distance and the holes to hold the sockets are of different diameters. While this is easy to figure out by hand, it's convenient to do it with a script. The report prints out the center locations for the holes and the divider settings to scribe the location of each hole center.
# Example
Suppose you had a set of fractional-inch-sized drills from 1/16 inch to 1/2 inch by 32nds of an inch. You want to make a 2 inch diameter cylindrical holder for these drills and have the drills equally spaced to make a pleasing layout. Here's a datafile that could be used (it's the file holes.drills in the holes.zip package):
# This file gives an example of making a "nice" cylindrical drill
# holder for a set of fractional inch drills. Suppose we want a
# layout for drill sizes from 1/16" to 1/2" by 32nds. Generate a
# layout for a main circle diameter of 2".

d = 1/32

2*d
3*d
4*d
5*d
6*d
7*d
8*d
9*d
10*d
11*d
12*d
13*d
14*d
15*d
16*d
Note the use of an assignment statement d = 1/32. You can use valid python expressions in the datafile to generate the diameters. The symbols from the math module are in scope, so you can write things like 12*cos(48*pi/180) to calculate twelve times the cosine of 48 degrees. There must be one assignment statement or diameter number per line. Blank lines and comments are ignored.
When the holes.py script was run with the command line
python holes.py holes.drills 2
the results were:
Main circle diameter = 2.000
        Polar ang., Ang. width,
    Dia x y degrees Chord degrees
-----------------------------------------------------------------------------
     0.06250 1.000 0. 0. 0.2138 3.582
     0.09375 0.9772 0.2125 12.27 0.2448 5.373
     0.1250 0.8962 0.4436 26.34 0.2759 7.167
     0.1562 0.7409 0.6716 42.19 0.3069 8.962
     0.1875 0.5023 0.8647 59.85 0.3379 10.76
     0.2188 0.1857 0.9826 79.30 0.3688 12.56
     0.2500 -0.1832 0.9831 100.6 0.3997 14.36
     0.2812 -0.5536 0.8328 123.6 0.4306 16.17
     0.3125 -0.8525 0.5228 148.5 0.4615 17.98
     0.3438 -0.9964 0.08438 175.2 0.4923 19.79
     0.3750 -0.9160 -0.4013 203.7 0.5230 21.61
     0.4062 -0.5881 -0.8088 234.0 0.5538 23.44
     0.4375 -0.06754 -0.9977 266.1 0.5845 25.27
     0.4688 0.5017 -0.8650 300.1 0.6151 27.11
     0.5000 0.9131 -0.4077 335.9 0.4169 28.96

Angle subtended by all circles = 243.1 deg = 4.243 rad
Gap angle between each circle = 7.794 deg = 0.1360 rad
The results give the circle diameters as they were encountered in the datafile. The x and y columns give the Cartesian coordinates of the hole centers. The first hole is on the x-axis and has a polar angle of zero. The Chord is the distance to the next hole on the main circle and can be used to set your dividers to lay out the holes. The Polar angle is the angle coordinate in polar coordinates for the circle's center, with the x-axis being the usual polar axis.
If you're willing to download the Postscript library from http://code.google.com/p/pygraphicsps/, you can supply the -g option to the script and it will generate a plot of the layout:
The circle diameters are written on the radial lines, the polar angle in the middle of these radial lines, and the chord (divider setting) is in red between the relevant circles.
# Program options
The usage statement is
Usage: holes.py [options] datafile diameter
  Will print a table of positions (Cartesian, angles, and chords) of
  the centers of the circles whose diameters are given in the datafile
  (one number per line) so that the angle between each of the circles
  is a constant. There are no implied units for the dimensions; use
  a consistent unit for your problem.

  The datafile may contain lines of the form 'a = b' which causes a
  variable named a to be defined. This variable can then be used in
  subsequent lines. b is a valid python expression. All the symbols
  from the math module are in scope. These assignment lines must be one
  per line. The diameter of the main circle (or the line length for the
  linear problem) is defined to be the symbol D.

  If you have the optional graphics library from
  http://code.google.com/p/pygraphicsps/, the script can generate a
  scaled drawing of the layout.

  The -l option causes the layout of the circles to be on a straight
  line. The diameter on the command line then becomes the distance
  between the circle's edges. An example of use is to lay out the holes
  to drill in a block of wood to hold a set of sockets.

Options:
    -D digits
        Number of decimal digits to round to.
    -d digits
        Number of significant figures in results. Default = 4.
    -g file
        Generate a Postscript drawing file of the layout.
    -l
        Lay out the circles on a line. The diameter on the command line
        is the distance between the edges of the circles.
    -r
        Lay out the circles in a clockwise direction (the default
        direction is counterclockwise).

Example: suppose the datafile contains
    1/4
    5/16
    3/8
    7/16
    1/2
  Running the script with the diameter 2 gives the output

  Main circle diameter = 2.000
        Polar ang., Ang. width,
     Dia x y degrees Chord degrees
 ----------------------------------------------------------------------------
     0.2500 1.000 0. 0. 1.097 14.36
     0.3125 0.3982 0.9173 66.53 1.149 17.98
     0.3750 -0.7277 0.6859 136.7 1.201 21.61
     0.4375 -0.8616 -0.5075 210.5 1.252 25.27
     0.5000 0.3086 -0.9512 288.0 1.176 28.96

  Angle subtended by all circles = 108.2 deg = 1.888 rad
  Gap angle between each circle = 50.36 deg = 0.8790 rad

Running the script with the same datafile and arguments '-l -D 2
datafile 0.2' gives the output

  Linear hole placement problem for line
    L = distance between circle edges = 0.2
        Hole
        i x Dividers Diameter
      -------- -------- -------- --------
        0 0.00 0.00 0.25
        1 0.48 0.48 0.31
        2 1.02 0.54 0.38
        3 1.63 0.61 0.44
        4 2.30 0.67 0.50
    Sum of diameters = 1.875
    Number of lengths L between holes = 4
    Overall length = 2.675

The number under the Dividers column is the distance to set your
dividers to in order to scribe the hole location from the previous hole
location (Dividers[i] = x[i] - x[i-1]).
By default, circles are placed on the main circle in counterclockwise fashion. If you want the circles to go clockwise, use the -r option.
If you see -.- in the printout, it indicates a number that was too small to print; you can regard it as zero.
# The algorithm
The algorithm used in the holes.py script is to determine the angle subtended along the main circle by each of the to-be-placed circles. Then the sum of these angles in radians is subtracted from 2 and this angle is divided by the number of circles to give the required angular spacing between circles. If the sum is greater than 2, there is no solution.
Here's a diagram of what it means for a circle to subtend an angle :
The main circle C is centered at O with diameter D = AB. Suppose the circle FGH is circle c_i . We need to calculate the angle %theta_i over 2 subtended by the circle's radius "EF" `=` r_i to determine how much of the circle C is taken up by the circle c_i . Let R = D/2. Then we have
%theta_i `=` 2 tan^{-1} 1 over sqrt{ left ( R over r_i right )^2 - 1}
As a check, I did an example layout using R = 75.15 mm and r = 68.3 mm. The calculated value of  was 130.7°; a protractor measured it at 130.25 ° and this was done by judging the full angle subtended by the circle with r for its radius by the eye and a straightedge. Then r was changed to 15 mm and  was measured to be 22.8°; the calculated value was 23.0°. These examples validate the formula.
Add up all of the angles found this way and subtract from 2 radians and divide by n, the number of circles to be placed. This gives the gap  between each circle.
To place the circles, pick the first circle and put its center at a polar angle of zero. Get %theta_i/2 for this circle and %theta_{i+1}/2 for the next circle to be placed; add the gap angle  and you have the position angle of the next circle as %theta_i/2 `+` %theta_{i+1} `+` %phi . Repeat for the remaining circles.
A subtlety is whether the pattern is to be placed in a counterclockwise or clockwise fashion, but this is simple to handle in the code -- just change all the polar angles to their negatives.