Waveform Generator
someonesdad1@gmail.com 7 Nov 2012

In engineering and science, we sometimes need various sampled waveforms such as sine waves, square waves, triangle waves, etc. While these can be generated as needed with numpy functions, I've found it's handy to have a python module that uses numpy to create the needed waveforms as numpy arrays. These can then be used for plotting, experimentation, setting up an arbitrary waveform generator, etc.
The relevant python module is called waveform.py. You can install it somewhere in your PYTHONPATH and you'll be able to use it. You'll also need to have numpy and scipy installed; if you want to plot the module's examples, you'll also need matplotlib.
# Overview of module
The module contains the Waveform object which can be used to construct various waveforms. Here's an example of generating a sine wave and plotting it with matplotlib:
from pylab import *
from waveform import Waveform
name, n = "sin", 100
w = Waveform(name, n)
x, y = w.xy() # Get abscissas and ordinates
plot(x, y, ".-")
title(f"Waveform({name}, {n})" % (name, n))
grid()
show()
The result is
The abscissas will be defined on [0, 1) and the ordinates are typically in the interval [-1, 1] for the internally-constructed waveforms.
Internally, the waveform is a numpy array defined to be one period and have unity amplitude. You'd then use the attributes to change the characteristics of the waveform. These attributes are only applied when you request a numpy array of the data using the xy() or __call__() methods.
Note that the last point of the waveform doesn't go to zero as you might expect. This is to allow these waveform arrays to be concatenated together to form longer periodic waveforms. If you do want the last point to be included, call the constructor as follows (n is the number of points and, here, must be an integer)
Waveform("sin", n + (1 + eps)/n)
where eps is a small number (1e-10 might be a good choice) to handle occasional roundoff problems.
Some of the features of the Waveform object are:
- It's easy to create elementary waveforms. Currently, the built-in ones are: cosine, dc, halfsine, haversine, noise, pulse, ramp, semicircle, sine, square, triangle.
- The module is easy to modify to let you define new types of waveforms.
- Waveform object attributes let you control various aspects of waveform creation.
- Scaling and adding a DC offset to a waveform are easy.
- Clipping and gating are also supported.
- Waveform objects can be added and subtracted to get composite waveforms by concatenation.
- Waveform objects can be multiplied together to simulate modulation [requires scipy].
- Waveform objects can be transformed by vectorized functions.
## The constructor
You can construct a Waveform object with one of the following constructors:
Waveform(name, size)	Makes one of the supported waveforms indicated by name with size points per period. It's straightforward to add support for new types of waveforms (modify the _make method).
Waveform(iterable)	The iterable must be convertible to a numpy array.
Waveform(numpy_array)	The numpy array will be flattened.
Waveform(waveform_object)	Creates a copy of an existing Waveform object.

Using a name in the constructor allows you to pick from waveforms like "sine", "square", "triangle", etc. See the Waveform._names array for the defined names.
The waveform is considered to be defined on the interval [0, 1).
## How it works
The elementary waveforms are generated internally with simple numpy commands (see Waveform._make() for details).
The internally-defined functions have the advantage that you can change the number of points in the waveform at any time and the data points will be regenerated. In contrast, a waveform that was initialized with an iterable or numpy array aren't quite as flexible. These types of waveforms have the name "unknown" to distinguish them from the internally-defined ones. They can also be resized, but this requires scipy's interpolation library.
For either type of waveforms, the data are stored in an internal array. This internal array is changed when:
- The waveform is resized.
- A transformation function is applied to the waveform using the xfm method.
- The Waveform object is multiplied by a constant or another Waveform object.
- A constant or another Waveform object is added to or subtracted from the Waveform object.
- The waveform has periodize() or normalize() called on it (Waveform object methods).
The typical use of the Waveform object is to create the desired waveform, set the attributes to indicate how you want the waveform changed, then get a numpy array containing a specified number of periods representing that waveform.
# Attributes
The internally-stored waveform is not changed by setting these values. It's only when the Waveform object outputs a numpy array representing the waveform that these attributes are applied. For example, suppose you defined a Waveform object to be a sine wave. Internally, the stored numpy array of the data (for now, call it data) ranges over the sine function's range for real arguments (i.e., the array's values lie in the interval [-1, 1]).
When you request a numpy representation of the waveform through the xy() method, the following things happen:
- A copy y is made of the raw data.
- y is gated (see below).
- y is clipped (see below).
- y is transformed to y*ampl + dc.
- The requested number of periods of the waveform is returned.
In the following table of attributes, the default value of the attribute is shown in angle brackets, such as <0>. The Waveform.reset() method can be used to set these attributes back to their default values.
ampl	Setting the amplitude scales all of the points of the waveform by this value. <1>
data	Returns a numpy array representing one period of the waveform. This is a read-only attribute and is the raw data stored internally (i.e., not modified by the attributes).
dc	Adds a constant to each point of the waveform. (The name comes from an electrical signal having a DC offset.) <0>
duty	Duty cycle for sine waves, cosine waves, triangle waves, square waves, pulses; this is the fraction of the period that the wave is positive or the pulse is nonzero. For sinusoids and triangle waves, the first derivative will be discontinuous if the duty cycle isn't 1/2. <0.5>
gates	Defines the gating intervals for the waveform. The value can be None or an iterable of pairs of numbers. This feature is used to set specified portions of the waveform to zero. See the section Gating below for more details. Fine control over the gating behavior is also affected by the lge and rle attributes. <None>
kind	Sets the type of interpolation to use (see the documentation for scipy.interpolate.interp1d for allowed values). This attribute is only used for resampling of waveforms of unknown type (i.e., changing the number of points in the waveform). <"linear">
lge	"left greater than or equal" / A Boolean used in gating to define the type of comparison at the left edge. If True, it is >=; otherwise it is >. For more details, see the Waveform._gate() method and the discussion of gating below. <True>
nclip	Clips the lower portion of the waveform at a specified fraction of the "negative" amplitude. See the discussion on clipping below. <1>
ndig	Sets the number of significant digits to print in the str() and repr() representations for the floating point numbers (uses the sig.py module). <3>
pclip	Clips the upper portion of the waveform at a specified fraction of the "positive" amplitude. See the discussion on clipping below. <1>
rle	"right less than or equal" / A Boolean used in gating to define the type of comparison at the right edge. If true, it is <=; otherwise it is <. For more details, see the Waveform._gate() method and the discussion of gating below. <True>
size	The number of points in the waveform. If you set this to a new value, the waveform is regenerated if it is not of the type "unknown"; for the latter case, it is done by using scipy's interp1d method (thus, you need to have scipy installed).
x	Returns a numpy array that represents the abscissas of the stored waveform. The values will be in the half-open interval "["0, `1")" . Note the returned array is for one period; if you want more periods, use the xy() method.
y	Returns a numpy array that represents the ordinates of the stored waveform. Note the returned array is for one period; if you want more periods, use the xy() method.
zero	Can either be None or a tuple of numbers (a, b) where a ≤ 0 and b ≥ 0. Negative numbers in the array that are between 0 and a are set to zero and positive numbers in the array that are between 0 and b are set to 0. This can help control small numbers caused by roundoff errors. If the value is None, no substitutions take place. <(-10-15, 10-15)>

Note that you can scale and generate an offset for a waveform in two ways. The first is using the attributes:
w = Waveform("sin", 100)
w.ampl = 4.5
w.dc = 3
x, y = w.xy()
which generates a sine wave of 100 points with amplitude 4.5 and a DC offset of 3.
The second way doesn't change the Waveform object w (however, the new Waveform object u is of unknown type):
u = w*a + b
where a and b are floating point numbers.
The repr() function can print the details of a Waveform object:
w = Waveform("sin", 8)
print(repr(w))
results in
Waveform(
Attributes:
  ampl = 1
  data = [0.00, 0.707, 1.00, 0.707, 0.00, -0.707, -1.00, -0.707]
  dc = 0
  duty = 0.500
  gates = None
  kind = linear
  lge = True
  name = sine
  nclip = 1
  ndig = 3
  pclip = 1
  rle = True
  size = 8
  x = [0.00, 0.125, 0.250, 0.375, 0.500, 0.625, 0.750, 0.875]
  zero = (-1.00e-15, 1.00e-15)
)
For using the Waveform object in a console environment, I suggest using using the pydoc script that comes with your python distribution. This gives a concise summary of the Waveform object's behavior.
## Gating
Gating allows setting portions of the waveform to zero. The gates attribute is set to a sequence of pairs of numbers; these numbers must be in the interval [0, 1]. These pairs of numbers define an interval of the waveform where the waveform's points should be set to zero. Let's look at an example.
Suppose the gates attribute is [(0, 0.1), (0.5, 0.7)]. These two intervals define the following function
This function is then multiplied by the waveform after converting it to an array of the same size as the data in the waveform.
The lge attribute determines the method of comparison at the left edge of the interval. If it is True, then the comparison is >=. This will include the left-hand border's point in the set to be zeroed. If lge is False, then the left-hand border's point is not included in the set to be zeroed. The rle attribute behaves analogously for the right-hand border.
An example can help make this clearer. The following script demonstrates the behavior on an array of integers by using the Waveform._gate() function:
import numpy as np
from waveform import Waveform
n = 20
w = Waveform("sin", n)
w.gates = [(1/8, 1/4), (7/8, 1)]
print("gates = " + str(w.gates))
print("lge = " + str(w.lge) + " rle = " + str(w.rle))
print(np.array(range(n)))
print(w._gate(np.array(range(n))))
w.lge = False
print("lge = " + str(w.lge) + " rle = " + str(w.rle))
print(np.array(range(n)))
print(w._gate(np.array(range(n))))
w.lge = True
w.rle = False
print("lge = " + str(w.lge) + " rle = " + str(w.rle))
print(np.array(range(n)))
print(w._gate(np.array(range(n))))
w.lge = False
print("lge = " + str(w.lge) + " rle = " + str(w.rle))
print(np.array(range(n)))
print(w._gate(np.array(range(n))))
The output is
gates = [(0.125, 0.25), (0.875, 1)]
lge = True rle = True
[ 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19]
[ 0 1 0 0 0 0 6 7 8 9 10 11 12 13 14 15 16 0 0 0]
lge = False rle = True
[ 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19]
[ 0 1 2 0 0 0 6 7 8 9 10 11 12 13 14 15 16 17 0 0]
lge = True rle = False
[ 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19]
[ 0 1 0 0 0 5 6 7 8 9 10 11 12 13 14 15 16 0 0 0]
lge = False rle = False
[ 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19]
[ 0 1 2 0 0 5 6 7 8 9 10 11 12 13 14 15 16 17 0 0]
The red numbers show where the gating was applied.
Here's a gated sine wave that's produced when waveform.py is run as a script:
## Clipping
The two attributes pclip and nclip determine the clipping levels. These levels are defined with respect to the mean of the waveform. Let the mean of the waveform y be ybar. Then if pclip is not 1, the portions of the waveform larger than ybar are clipped to lie within ybar + pclip*ymax where ymax is the largest value of y. if nclip is not 1, the portions of the waveform smaller than ybar are clipped to lie within ybar - nclip*ymin where ymin is the smallest value of y.
Here's an example script:
from waveform import Waveform
n = 100
w = n*Waveform("sin", n)
x, y = w.xy()
print("Unclipped:")
print(str(y.astype(int)))
# Now clip the waveform
w.pclip = 0.9
w.nclip = 0.75
x, y = w.xy()
print("\nClipped:")
print(str(y.astype(int)))
Here are the results:
Unclipped:
[ 0 6 12 18 24 30 36 42 48 53 58 63 68 72 77
   80 84 87 90 92 95 96 98 99 99 100 99 99 98 96
   95 92 90 87 84 80 77 72 68 63 58 53 48 42 36
   30 24 18 12 6 0 -6 -12 -18 -24 -30 -36 -42 -48 -53
  -58 -63 -68 -72 -77 -80 -84 -87 -90 -92 -95 -96 -98 -99 -99
 -100 -99 -99 -98 -96 -95 -92 -90 -87 -84 -80 -77 -72 -68 -63
  -58 -53 -48 -42 -36 -30 -24 -18 -12 -6]

Clipped:
[ 0 6 12 18 24 30 36 42 48 53 58 63 68 72 77 80 84 87
  90 90 90 90 90 90 90 90 90 90 90 90 90 90 90 87 84 80
  77 72 68 63 58 53 48 42 36 30 24 18 12 6 0 -6 -12 -18
 -24 -30 -36 -42 -48 -53 -58 -63 -68 -72 -75 -75 -75 -75 -75 -75 -75 -75
 -75 -75 -75 -75 -75 -75 -75 -75 -75 -75 -75 -75 -75 -75 -75 -72 -68 -63
 -58 -53 -48 -42 -36 -30 -24 -18 -12 -6]
Here's a clipped sine wave that's produced when waveform.py is run as a script:
## Resampling
When you set the size attribute and the waveform type is unknown, the new waveform's data points need to be calculated from the old waveform's data points. This contrasts to the built-in waveform types where they are just reconstructed via the _make() method.
This changing the number of data points is called resampling. There are many ways of doing this task, but I chose to use scipy's interp1d interpolation function because it is so easy to use. The default is to use linear interpolation, which should be adequate for most tasks.
# Methods
__call__(num_periods)	Calling the Waveform object with a number returns a numpy array of that number of periods. num_periods defaults to 1.
normalize()	Scales each point in the waveform such that the maximum absolute value is unity. The waveform type will become unknown.
periodize(num_periods)	Replace the waveform by num_periods of the waveform. Thus, the new size will be int(num_periods*old_size). The waveform type will become unknown, as it can't be resampled except by interpolation.
reset()	Reset all attributes to their default values.
xfm(f, *args, **kw)	Apply a function f to the data in the array to transform the data. f is a univariate function that can operate on a numpy array; if args is not empty, then these arguments are appended. kw contains any keyword arguments that must be passed to f. The waveform type will become unknown.
xy(num_periods)	Returns a tuple (x, y) of the abscissas and ordinates of the waveform for the stated number of periods. This method would typically be used to get the data for plotting the waveform. Note x's values will be on "["0, `1")" . num_periods defaults to 1.

# Defining new waveforms
To add another waveform type, the Waveform._make() method should be modified appropriately. The existing definitions will be examples. The primary task is to assign the waveform's data points to the self._data attribute.
You also need to assign a unique name to the waveform and put it in the Waveform._names array.
# Examples
## Simulated SCR waveform
from pylab import *
from waveform import Waveform
w = Waveform("halfsine", 100)
w.gates = [(0, 0.25)]
x, y = (w - w).xy(2)
plot(x, y, ".-")
title("Simulated SCR Waveform")
grid()
show()
generates the following plot:
Remember that w - w in the code means concatenation after inverting the second waveform (otherwise you might think it was a subtraction that should result in all zeros).
## Trapezoidal waveform
Suppose we wanted to create a bipolar trapezoidal waveform with one half period as follows:
This is straightforward once we decide on the number of waveform points we want in the interval from 0 to 1. Suppose we want 100 points. Then the following code will generate the waveform:
from pylab import *
from waveform import Waveform
w1 = Waveform("ramp", 100)
w2 = Waveform("dc", 2*100) + 1
w3 = -Waveform("ramp", 3*100) + 1
w4 = Waveform("dc", 100)
w = w1 + w2 + w3 + w4
x, y = (w - w).xy()
plot(x, y)
title("Trapezoidal Waveform")
grid()
a = 1.05
ylim(-a, a)
show()
which results in
## Staircase waveform
from pylab import *
from waveform import Waveform

n, steps = 20, 8
w = Waveform("dc", n)
for i in range(1, steps + 1):
    w += Waveform("dc", n) + i
w.normalize()
x, y = w.xy()
plot(x, y)
title("Staircase Waveform")
grid()
a = 0.05
ylim(-a, 1 + a)
show()
results in
## Modulation by multiplication
from pylab import *
from waveform import Waveform

n = 100
w = Waveform("sin", n)
w1 = Waveform(w)
w1.xfm(abs)
w = Waveform(w(10))
x, y = (w*w1).xy()
plot(x, y, "-")
title("Sine modulated by abs(sine)")
grid()
show()
results in
## "MW" waveform
You'll understand the name once you see the plot... This shows a simple transformation of a sine wave by the use of the absolute value:
from pylab import *
from waveform import Waveform
n = 100
w = Waveform("sin", n)
w.xfm(abs)
x, y = (w - w).xy()
plot(x, y)
title('"MW" Waveform (two sine humps')
grid()
show()