thd.py Program Output
someonesdad1@gmail.com 2005
Updated 1 Dec 2013
The thd.py program is a script written in python to output various things of interest with respect to threads. The program is based on the formulas of the inch-based ASME [asme] standard.
# Usage
Here's the usage statement:
Usage: thd.py [options] thread_size

Prints thread information for the indicated external thread. Examples:

    thd.py n6-32
        US numbered machine screw sizes are preceded by an 'n'
    thd.py 0.25-20
    thd.py 0.25 20
    thd.py 1/4-20
    thd.py 1/4 20
    thd.py 1 1/2-6
    thd.py 1 1/2 6
    thd.py -m 6 1

Options
    -a frac Min & max wire sizes for this thread (use -h for details)
    -b Show lathe threads closest to metric pitches
    -c num Specify class 1, 2, or 3 thread (2 is default)
    -h Detailed help
    -l List the taps and dies on hand.
    -L loe Change the length of engagement from 1. Units are the
        basic major diameter.
    -m Metric threads: dia in mm, pitch in mm
    -o Show threads within 5% of given OD
    -t Show threads within 5% of given tpi
    -T Print table of UNC, UNF, UNEF threads
    -u Show common UNC and UNF sizes
    -w dia Specify size of thread wire to use

Use -h for more detailed help.
This script will produce information that is slightly different than that given e.g. in the thread tables in Machinery's Handbook. It's not clear to me which should be regarded as correct, the formulas or the tables. Since the tables are what are commonly available, I would assume most people would assume the tables are correct. However, they were likely generated from formulas for consistency, so a discrepancy might be caused by a table mistake. Regardless, I wouldn't recommend using the script for serious or critical work without checking its numbers against a standard table. Spot checks of the values indicate the discrepancies are probably rounding differences, as the differences are typically a few 0.0001" at most (and these differences are mentioned in the standard as due to rounding).
If thread_size is a single number, it is the pitch in inches (mm if the -m option is given). An abbreviated table of information is printed for that pitch.
The script lets you calculate with dimensions in mm by using the -m option. The numbers presented are calculated from the AMSE standard's formulas; these may or may not match the metric standards, so it's your responsibility to verify the numbers.
The calculations are for thread lengths of engagement up to 1.5 times the major diameter. You'll want to consult the ASME standard for larger lengths of engagements because the formulas change.
The -l option shows me the taps and dies I have on hand. Obviously, this is person-specific, so you'll want to edit the global variable my_sizes in the script to reflect your own tools.
The wires global variable contains the diameters of the on-hand measuring wires. You'll want to customize this to the set of wires you use.
The thread formulas from the ASME standard are encapsulated in the associated python library of asme.py.
The -T option causes the script to print out a table of class 2 thread information given in my 19th edition of Machinery's Handbook. This is a rather dense table of 30+ pages covering inch-sized threads up to 4 inches in major diameter. You can print this table out and check it against the book's values to get a flavor for the script's output accuracy.
The -b option can be handy if you have an inch-only lathe like I do. I have cut a few metric threads using inch-based threads and, if the length of engagement is small, the threads work fine (for example, I made a lens adapter for my old Canon camera with a metric thread and it worked fine). The key is to compare the pitches and length of engagement -- a mismatch over a short length of engagement may be OK. One clever trick I've not tried (but read about in a 100-year-old book) is to set the tailstock over to cut a taper but set the taper attachment to the opposite taper to make it cut a non-taper. Fine adjustments in a thread's pitch can be made this way.
# Output
We'll discuss each output line in the program's output for a particular thread dimension.
Note that the program may produce output that is different from that published in tables.
Here's the program's output for a 1/2 - 13 UNC class 2 thread:
        inches mm
        ------ ---
Nominal diameter 0.5000 12.70
Threads per inch or mm 13.0 0.51
Length of engagement 0.5000 12.70
Seller's recommended tpi 12.6
Thread class 2
Pitch 0.0769 1.95
Allowance 0.0015 0.04
Tensile area, in^2 or mm^2 0.140189 90.44

External thread
    Major diameter
        Max 0.4985 12.66
        Min 0.4877 12.39
        Tolerance 0.0109 0.28
    Pitch diameter
        Max 0.4485 11.39
        Min 0.4436 11.27
        Tolerance 0.0050 0.13

Internal thread
    Minor diameter
        Max 0.4336 11.01
        Min 0.4167 10.58
        Tolerance 0.0169 0.43
    Pitch diameter
        Max 0.4565 11.59
        Min 0.4500 11.43
        Tolerance 0.0065 0.16

Measurements over wires
    Min wire size 0.033 0.85
    Max wire size (95%) 0.075 1.90
    Best wire size 0.044412 1.13
        Meas. over best wires, max 0.5153 13.09
        Meas. over best wires, min 0.5103 12.96
    On-hand wire size 0.045 1.14
        Meas. over wires, max 0.5170 13.13
        Meas. over wires, min 0.5121 13.01

Tap drills
     50% thread 0.4500 11.43 29/64
     55% thread 0.4450 11.30 7/16
     60% thread 0.4400 11.18 7/16
     65% thread 0.4350 11.05 7/16
     70% thread 0.4301 10.92 7/16
     75% thread 0.4251 10.80 27/64
     80% thread 0.4201 10.67 27/64
     85% thread 0.4151 10.54 Z
     90% thread 0.4101 10.42 Z
     95% thread 0.4051 10.29 Y
    100% thread 0.4001 10.16 X

Sharp V thread with National Form flat on OD, compound at 29 deg
    Double depth 0.117 2.96
    Compound feed, DD/cos(29) 0.133 3.39

Unified thread, compound at 29 deg
    Flat on form tool 0.010 0.24
    Double depth 0.100 2.54
    Compound feed, DD/cos(29) 0.114 2.90
In the following, MMC means “maximum material condition”. For an external thread, this means the OD of the thread is at a maximum. For an internal thread, this means the minor diameter is at the minimum.
Nominal diameter	Thread’s nominal outside diameter.
Threads per inch	The inverse of the pitch in inches.
Length of engagement	How many basic major diameters of the thread are engaged.
Seller's recommended tpi	Seller's was a mechanical engineer in the 1800's who recommended a US thread standard and today's threads are derived from his work. He provided a formula "pitch in inches" `=` a sqrt{D + 5/8} - 0.175 where a is 0.24 for threads 1/4 inch or larger and 0.23 for smaller threads.
Thread class	1, 2, or 3. Class 1 threads are for rough work and are loose. Class 2 threads are for normal work. Class 3 threads are for close work.
Pitch	Distance between thread crests (in a single lead thread).
Allowance	Geometrical clearance between the MMC external thread and the MMC internal thread. Gotten by subtracting the external thread major diameter max from the internal thread minor diameter min.
Tensile area	Geometrical cylinder representing the contiguous material in tension. Used for estimating the tensile strength and shear strength of the thread.
External thread, major diameter, max	Maximum allowed major diameter. Note that this is typically less than the nominal diameter, which allows for a cleaning cut before threading.
External thread, major diameter, min	Minimum allowed major diameter. For the ½-13 thread, this dimension is 0.012 inches below the nominal diameter, which allows for a significant cleaning cut before threading.
External thread, major diameter, tolerance	Difference between the maximum and minimum major diameters. This gives you a feeling for how much material you have to play with.
External thread, pitch diameter, max	Maximum pitch diameter for an external thread. The pitch diameter (sometimes called the effective diameter) is the diameter of the cylinder that cuts the thread in half.
External thread, pitch diameter, min	Minimum pitch diameter for an external thread.
External thread, pitch diameter, tolerance	Difference between the maximum and minimum external pitch diameters.
Internal thread, minor diameter, max	Maximum minor diameter for an internal thread. Before cutting an internal thread on the lathe, this would be the largest hole you can bore in the stock.
Internal thread, minor diameter, min	Minimum minor diameter for an internal thread. Before cutting an internal thread on the lathe, this would be the smallest hole you can bore in the stock. Also is the MMC for an internal thread.
Internal thread, minor diameter, tolerance	Difference between the maximum and minimum minor diameter for an internal thread.
Internal thread, pitch diameter, max	Maximum pitch diameter of an internal thread.
Internal thread, pitch diameter, min	Minimum pitch diameter of an internal thread.
Internal thread, pitch diameter, tolerance	Difference between the maximum and minimum pitch diameter for an internal thread.
Min wire size	When measuring the pitch diameter of an external thread with the three wire method, this is the minimum wire size you can use for this pitch of thread.
Max wire size (95%)	When measuring the pitch diameter of an external thread with the three wire method, this is the maximum wire size you can use for this pitch of thread.
Best wire size	When measuring the pitch diameter of an external thread with the three wire method, this is the best wire size you can use for this pitch of thread. Here, best means the wire will contact the flank of the thread at the pitch diameter.
Meas. over best wires, max	Measurement over best wires for the maximum pitch diameter allowed for this thread.
Meas. over best wires, min	Measurement over best wires for the minimum pitch diameter allowed for this thread.
(On-hand wires) Meas. over wires, max	Measurement over on-hand wires for the maximum pitch diameter allowed for this thread. Note: the on-hand wires are entered into the program’s code and allow you to customize the program to the wires you have on hand.
(On-hand wires) Meas. over wires, min	Measurement over on-hand wires for the minimum pitch diameter allowed for this thread.
Tap drills, 50% thread	Tap drill to use to get approximately a 50% thread with a tap. The percentage is a measure of how much the tapped internal thread represents a UN thread. Smaller than 100% means the minor diameter is larger than allowed by the specified thread dimensions. Thread percentages smaller than 100% are used because they make tapping much easier. Standard practice for normal shop grade threads is to use about 60% to 75% threads.
Tap drills, 55% thread	Tap drill to use to get approximately a 55% thread with a tap.
Tap drills, 60% thread	Tap drill to use to get approximately a 60% thread with a tap.
Tap drills, 65% thread	Tap drill to use to get approximately a 65% thread with a tap.
Tap drills, 70% thread	Tap drill to use to get approximately a 70% thread with a tap.
Tap drills, 75% thread	Tap drill to use to get approximately a 75% thread with a tap.
Sharp V, Double depth	For a geometrically perfect 60 thread, this is the depth you would have to feed in a sharp vee-shaped cutting tool on the cross slide to cut this thread. Most home shops cut sharp vee threads.
Sharp V, Compound feed	This is the amount you feed in a sharp vee-shaped cutting tool on the compound slide when the compound is set to 29. Most threading on the lathe is done by feeding the compound in; the cross slide is used to back out and reposition the cutting tool at its “zero” position.
Unified, Flat on form tool	This is the flat you would grind on the tip of the cutting tool if you wanted to cut a Unified thread. This flat is different for every Unified pitch, so you technically would need a cutting tool for each pitch you’re going to cut.
Unified, Double depth	For a geometrically perfect Unified thread, this is the depth you would have to feed in a Unified cutting tool on a lathe's cross slide to cut this thread.
Unified, Compound feed	This is the amount you feed in a Unified cutting tool on the lathe's compound slide when the compound is set to 29. Most threading on the lathe is done by feeding the compound in; the cross slide is used to back out and reposition the cutting tool at its “zero” position.

# References
mh	E. Oberg and F. Jones, Machinery's Handbook, 19th ed., Industrial Press, 1971.
asme	ASME B1.1-1989 standard