Using a Table Saw to cut a Cove
someonesdad1@gmail.com 27 Dec 2012
Updated 25 Oct 2014
Occasionally in the shop one needs to make a cove in a workpiece. A cove is a concave cut in a material with a cross-section that is a segment of a circle. Coves are commonly used on various types of wooden molding. In metal, the usual tool is a ball-end milling cutter or a tilted end mill. In wood, a routing or shaper bit can be used. What happens to a homeowner like me, though, is that one needs to cut a cove for which a cutter doesn't exist -- or you don't want to spend a bunch of money for a cutter you know you'll use only once.
You can cut approximate coves in wood on your table saw. This document looks at two ways of setting the table saw up to do this.
Here are the key dimensions and the symbols we'll use:
The width of the cove is w and the height is h. D is the diameter of the circle that the segment comes from.
# The principle
Here's what we want to cut, a cove of width w and depth h (from a circle of diameter D):
If the cove's diameter D matched the saw blade's diameter, then we could push the workpiece past the saw blade in the direction parallel to the axis of rotation, raising the saw blade a little for each cut. But few coves will have the required dimensions.
Figure 1
The insight into the method comes from imagining that you feed the work into the saw blade at an angle to the axis of rotation. This "rotates" the saw blade an angle θ about an axis normal to the saw's table and creates an ellipse with the following geometry:

Thus, the "cove" will geometrically be an ellipse that passes through the three points P1, P2, and P3. The utility of the method comes from the fact that if w and h are "small" relative to the saw blade's radius D/2, this is a reasonable approximation to a circular form.
The saw blade is a fixed diameter and, in general, it's a circle that won't fit through the three points defining the cove. But if the saw blade is "rotated" about the y axis, this generates an ellipse which passes through the three points. For decorative woodworking, the deviation from a circular cove cross-section is likely not important. The included script can calculate the maximum difference between the desired circular form and the approximating elliptical form.
# Approximate method
A fixture for determining the required angle to feed the workpiece is based on a navigator's parallel rule:
Boards A and B are constrained to remain parallel to each other because of the pinned joints. The distance between them is set to the desired cove width w. The saw blade is raised until it is the desired height h above the table (this is the desired cove depth). Then the fixture is placed over the blade and the fixture is rotated about an axis perpendicular to the table so that the saw blade is contacted by boards A and B. This gives the required angle to set the fence for cutting the cove.
If you're going to use this for making a number of different coves, join the boards with e.g. flat head bolts and wing nuts so that it can be adjusted to size. Otherwise, make it rigidly from some scrap boards.
Here's another fixture you can make (an adjustable "tee-square") that uses the saw table's edge as a reference:
Once things are positioned correctly, you'd clamp board A to the table saw's top.
# Analytical method
For more fussy work, you can calculate the required angle θ for the fence:
stack { alignl %theta `=` {alignc cos^{-1} w over sqrt{u^2 + t^2} `+` tan^{-1} t over u}# alignl u `=` 2 sqrt{ h(D - h) } }

where
θ = fence angle with respect to the saw blade's axis of rotation
w = width of cove
h = depth of cove
t = kerf width of saw blade
D = diameter of saw blade.
To be able to evaluate this equation, you'll need a calculator that can calculate inverse trigonometric functions. If you don't have such a calculator, you can still do the computation using a table of trigonometric values.
Suppose we want to cut a cove 5 mm deep and 50 mm wide. The saw blade diameter is 250 mm and the kerf width is 2 mm or
h = 5
w = 50
D = 250
t = 2
Substituting these numbers into the above equation, we have
u = 2 sqrt{ 5(250 - 5) } = 70
and
stack { alignl %theta `=` {alignc cos^{-1} 50 over sqrt{70^2 + 2^2} `+` tan^{-1} 2 over 70} # alignl phantom %theta `=`{alignc cos^{-1} 50 over sqrt{4904} `+` tan^{-1} 1 over 35} # alignl phantom %theta `=` 44.44° `+` 1.64° `=` 46.08° }
The fence needs to be set to this angle with respect to the axis of rotation of the blade (looking down in plan view).
If you don't have a calculator that has the trig functions, you can use the following table for the inverse cosine (the angle is given in degrees); linear interpolation will give you roughly table accuracy for arguments up to around 0.8.

Since the blade width will be a small number, the inverse tangent table can be smaller:
The inverse tangent is very linear for small arguments, so linear interpolation gives full table accuracy.
## Using the script
For cutting one cove, the formula is probably the tool of choice. If you want to perform the calculations for coves of different dimensions, the cove.py script may be of use. It allows you to enter the cove's dimensions in inches or mm and prints out the answer in both inches and mm for convenience.
The basic usage is (run the script with no input to get a usage statement)
Usage: /d/pylib/pgm/cove.py [options] width height
  Prints the fence angle (with respect to the blade rotation axis)
  needed for a table saw to cut a cove of specified dimensions. The
  input units are inches unless you use the -m option.

  width is the width of the cove at the surface of the workpiece.
  height is the depth of the cove (i.e., how high above the table
  you'll set the blade to make the deepest part of the cut).

Options:
    -d diam
        Sets the diameter of the saw blade. Since you'll probably use
        the program with one saw blade size, you can set the Diameter
        global variable to your saw blade's diameter for convenience.
    -i
        Include instructions for cutting the cove.
    -k kerf_width
        Set the kerf width of the blade.
    -m
        Set the input units to mm.
    -x X_width
        Set the X dimension for your table saw. See the cove.pdf
        document for an explanation.
where width is the cove's width (w in the formulas) and height is the depth of the cove (h in the formulas). Inches are the default units; you can change to mm units by using the -m option (make sure it is the first argument on the command line). The script internally uses mm for all calculations; if you work exclusively in mm, change the line that sets the default value for d["-m"] in the ParseCommandLine() function to True to let you use mm by default (then the -m option turns on inch units).
To solve the example problem, use the command
python cove.py -m -d 250 -k 2 50 5
yields the result
Cutting a cove:
  Blade diameter 9.843 in 250.00 mm
  Cove width 1.969 in 50.00 mm
  Cove height 0.197 in 5.00 mm
  Kerf width 0.079 in 2.00 mm
  X dimension 23.600 in 599.44 mm
  Y dimension 22.730 in 577.34 mm
  Max diff from circle 0.004 in 0.09 mm
  Fence angle (theta) 46.08 degrees = atan(X/Y)
        0.8042 radians
The Max diff from circle line gives the maximum difference between a circular cove form and the approximating elliptical form cut by the table saw.
You can set the global variables Diameter, Kerf_width, and X_width in the script for your particular saw and not have to use the -d and -k options.
# Derivation
This section derives the formula for cutting the cove. Our goal is to determine the rotation angle θ as a function of D (diameter of saw blade), w (width of cove), and h (cove depth/height).
The desired width w of the cove in Error: Reference source not found can be gotten by rotating the circle about the y axis by (roughly) an angle whose cosine times the unrotated width gives the desired width. A complication is that the saw blade has a finite thickness and the rotation "exposes" part of this thickness which we need to account for:
Here's a picture of the geometry looking down on the top of the table saw (plan view; the thickness t of the saw blade is exaggerated):
Let
ABEF is the intersection of the saw blade with the table top
 = angle of fence EG with respect to axis of blade rotation in plan view
EH is parallel to the blade's axis of rotation
t = thickness of saw blade = width of kerf = AB
v = AD - BC = t sin %theta = width due to "exposing" back of blade by rotation θ
h = depth of cove
D = diameter of saw blade
w = width of cut cove = "AD" `=` u cos %theta `+` t sin %theta
u = width of cove for θ = 0
The dashed lines show the width of a cove cut into a workpiece fed into the blade at the angle θ to the blade's rotation axis in the plan view. If you imagine your eye at point G and that you're looking along the direction GE, you'll see the "rotated" width of the exposed blade u as the desired distance w and it includes the small correction v for the exposed back edge of the saw blade.
Looking down the axis of blade rotation, we have
The Pythagorean theorem gives
D^2 over 4 `=` a^2 `+` b^2 `=` left (u over 2 right )^2 `+` left ( D over 2 `-` h right )^2
Solving for u gives
u `=` 2 sqrt{h (D - h)}
We also have
stack { alignl w `=` "BC" `+` v # alignl "BC" `=` u cos %theta # alignl v `=` t sin %theta }
giving
w `=` u cos %theta `+` t sin %theta	(1)

This equation gives the required angle θ implicitly; we can solve for the angle θ as follows. Use the formula for the cosine of a difference of two angles (this is essentially the conversion of a vector in the plane from rectangular coordinates to polar coordinates):
A cos(%theta - x) = {A cos x} underbrace u cos %theta + {A sin x} underbrace t sin %theta
To find A and x, solve the simultaneous equations
matrix { stack { alignl A cos x = u # alignl A sin x = t } # ~~~~size 18 drarrow ~~~~ # stack { alignl x = {alignc tan^{-1}(t/u)} # alignl A = sqrt{u^2 + t^2} } }
Thus, equation (1) becomes
w `=` sqrt{ u^2 + t^2 }cos( %theta - tan^{-1} (t/u) )
which can be solved for %theta to give
stack { alignl %theta `=` {alignc cos^{-1} w over sqrt{u^2 + t^2} `+` tan^{-1} t over u}# "where" # u `=` 2 sqrt{ h(D - h) } }	(2)

If you're willing to approximate t by zero for rough work, this formula simplifies to
%theta `=`cos^{-1} w over {2 sqrt{ h(D - h)}}	(3)

Equation (3) is the angle formula for a saw blade with no thickness.
## Setting the table saw's fence
We have the angle θ we must set the fence to. How do we set the fence to this angle? Here's the method I use:
The distance y is the width of the saw's table parallel to the plane of the blade. On my saw, this dimension is 27 inches. The value x/y is the tangent of the angle θ. Then we can calculate that
x `=` y over {tan %theta}
We'll mark this value on the front of the table to the left of the right hand table slot. Use a sufficiently long board that has a straight edge for the fence. Clamp the board at the proper angle, using the edge of the table slot and the mark you made. Raise the saw blade to the depth you are going to make the cove. Then measure the perpendicular distance to the front of the saw blade where it intersects the plane of the table. Adjust this distance to the value you need by moving the fence parallel to its current position. Clamp the board in position.
You're now ready to cut the cove. Lower the blade to flush with the table top, then raise the blade about 1 to 1.5 mm at a time and make a cut. Repeat this until the cove is the desired depth.
If you followed these directions and set the distances accurately, you should have a cove close to what you designed. I use a height gauge to set the height of the saw blade. On my table saw, a 45 degree angle requires measuring x and y dimensions of about 600 mm. If I made a 10 mm mistake in measurement, the resulting angle θ would be in error by about
tan^{-1}(1 + 1 over 60) - 45° approx 0.5°
This error, in turn, would have meant that the cove width would have been in error by about 0.1 mm. For most purposes in woodworking, this should be adequate for your needs.
So, is all this work worth it? If you just need a cove and you're not concerned about precision, I'd recommend that the fixtures mentioned in the section Approximate method. For more precise work, use the formula (2) to set up a fence. However, remember that this is still an approximation (i.e., the cut section is an ellipse, not a circle).
## Goodness of the approximation
I wrote a compare.py script that helps assess how good the table saw approximation to a circular cove is (send me an email if you'd like a copy). If you have sympy installed, it will print out the equations for the curves. If you have numpy/matplotlib installed, you'll get the following graph:

### Constraints
u sets the maximum width for the cove.
The saw can only expose a certain amount of blade; this determines the maximum value for h.
u as a function of h ( u `=` 2 sqrt{ h(D - h) } ) for a D = 250 mm diameter saw blade: